## Slide 1
Microprocessor & Computer Architecture (μpCA)
UE23CS251B
Session - 10

## Slide 2
Microprocessor & Computer Architecture (μpCA)
UE23CS251B
Instruction Encoding - 1

## Slide 3: Instruction Encoding
You showed me
ADD R0,R0,R1
But what is this in Binary

## Slide 4: What is an ARM Instruction?
An instruction specifies a Conditional Execution Code (Condition), the OP Code, Two or Three Registers (Rn, Rd, and Rm), and some other information
Example: Data Processing Instruction
OPcode{condition}{S} Rd,Operand1,Operand2

## Slide 5: Condition
Fifteen different conditions may be used: these are listed in Condition code summary.
The sixteenth (1111) is reserved, and must not be used.
In the absence of a suffix, the condition field of most instructions is set to "Always" (sufix AL). This means the instruction will always be executed regardless of the CPSR condition codes.
The ARM condition code field
28
31
24
20
16
12
8
4
0
Cond

## Slide 6: The Condition Field
28
31
24
20
16
12
8
4
0
Cond
0000 = EQ - Z set (equal)
0001 = NE - Z clear (not equal)
0010 = HS / CS - C set (unsigned higher or same)
0011 = LO / CC - C clear (unsigned lower)
0100 = MI -N set (negative)
0101 = PL - N clear (positive or zero)
0110 = VS - V set (overflow)
0111 = VC - V clear (no overflow)
1000 = HI - C set and Z clear (unsigned higher)
1001 = LS - C clear or Z (set unsigned lower or same)
1010 = GE - N set and V set, or N clear and V clear (>or =)
1011 = LT - N set and V clear, or N clear and V set (>)
1100 = GT - Z clear, and either N set and V set, or N clear and V set (>)
1101 = LE - Z set, or N set and V clear,or N clear and V set (<, or =)
1110 = AL - always
1111 = NV - reserved.

## Slide 7: Data Processing Instruction

## Slide 8: Data Processing Instruction Example 01:
Ex:
ADD R1, R0, R2
1110 000 0100 S Rn Rd 00000000 Rm
1110 0000 1000 0000 0001 0000 0000 0010
E0801002
R2
R1
R0
ADD
Always

## Slide 9: Data Processing Instruction

## Slide 10: Data Processing Instruction

## Slide 11: Data Processing Instruction Example 02:
Ex:
ADDS R1, R0, R2 LSR #2
1110 000 0100 S Rn Rd Shift Rm
1110 000 0100 S Rn Rd 00010 01 0 Rm
1110 0000 1001 0000 0001 0001 0010 0010
ADDS
R0
E0901122
R1
R2
LSR
#2
Shift is specified as immediate

## Slide 12: Data Processing Instruction Example 03:
Ex:
ADDS R1, R0, R2 LSR R4
1110 000 0100 S Rn Rd Shift Rm
1110 000 0100 S Rn Rd 0100 0 01 1 Rm
1110 0000 1001 0000 0001 0100 0011 0010
ADDS
R0
R1
R2
LSR
R4
E0901432
Shift is specified in Register

## Slide 13
√
√
√
√
√
√

## Slide 15
THANK YOU
V R BADRI PRASAD
badriprasad@pes.edu
Department of Computer Science and Engineering