## Slide 1
Microprocessor & Computer Architecture (μpCA)
UE22CS251B
Session - 5A

## Slide 2
Microprocessor & Computer Architecture (μpCA)
UE23CS251B
Additional Programs

## Slide 3: Program-1 : Convert a given 2 digit hexadecimal number to ASCII CODE and store the result in the memory location X and X+1 using ARM7TDMI – ISA.
Example: (54)10 to ASCII code :
Mask the LS byte.
54 and 0xF0 gives 50.
shift 50 right by 4 times
50 will be 05.
Now, 05 && 0x30
Results in 0x35.
Repeat the same for the LS byte.
Mask the MS byte.
54 and 0x0F gives 04.
Now, 04 && 0x30
Results in 0x34.
;ARM7TDMI – ISA code:
.TEXT
LDR R3, =X
MOV R1, #0x54
AND R0, R1, #0xF0
MOV R0, R0, LSR #4
ORR R0, R0, #0x30
STR R0, [R3]
AND R2, R1, #0x0F
ORR R2, R2, #0x30
ADD R3, R3, #4
STR R2, [R3]
.DATA
X: .WORD 0,0

## Slide 4
Program - 2: Write a program using ARM7TDMI – ISA to find the largest 32 bit element stored in an array A.
.DATA
A: .WORD 10,20,30,40,50
.TEXT
LDR R1,=A
LDR R0, [R1] ; Initially , set first element as the largest element (stored in register R0].
MOV R3, #0 ; Count Register
LOOP: LDR R2, [R1, #4]! ; load the next element
CMP R0, R2 ; compare
BLT Less ; if the previous element is less than next element then store the largest element in register R0.
L1: ADD R3, R3, #1
CMP R3, #4
BNE LOOP
B EXIT
Less: MOV R0, R2
B L1
EXIT: SWI 0X011

## Slide 5
Program - 3: Convert the following C code to ALP using ARM7TDMI – ISA, code snippet
C statement: while( save[i] == k)
i+=1;
.TEXT
LDR R1, =K ; ADDRESS K
LDR R0, [R1] ; VALUE of K
LDR R2, =SAVE ; SAVE is the starting address of the array
MOV R3, #0 ; VALUE of I
LOOP: ADD R5, R2, R3, LSL #2 ; R5 = SAVE+I*4
LDR R6, [R5,#0] ; R6 = [R5]
CMP R0, R6
BNE EXIT ; REPEAT if save[I]==K
ADD R3, R3, #1
CMP R3, #5
BNE LOOP
EXIT: SWI 0X011
.DATA
K: .WORD 5
I: .WORD 0
SAVE: .WORD 5, 5, 5, 50, 35, 40

## Slide 6: Program – 4: Consider the following c code snippet. Write the compiled ARM assembly code. Use ARM7TDMI – ISA.
int example( int g, int h, int I, int j)
{ int f;
f= (g+h)-(i+j);
return f;
}
.TEXT
LDR R4,=F
MOV R0, #5 ;G
MOV R1, #10 ;H
MOV R2, #1 ;I
MOV R3, #4 ;J
BL example
STR R0, [R4]
SWI 0X011
example:
SUB R13, R13, #12
STR R6, [R13,#8]
STR R5, [R13,#4]
STR R4, [R13,#0]
ADD R5, R0, R1 ; G+H
ADD R6, R2, R3 ; I+j
SUB R4, R5, R6 ;F= (G+H)-(I+J)
MOV R0, R4 ;RETURNS F THROUGH R0.
LDR R4,[R13,#0]
LDR R5,[R13,#4]
LDR R6,[R13,#8]
ADD R13, R13, #12
MOV PC, LR
.DATA
F: .WORD 0

## Slide 7: Program – 4: Consider the following c code snippet. Write the compiled ARM assembly code. Use ARM7TDMI – ISA. ; Note: this is a function sub program. Pass parameters to funcion on stack.
int example( int g, int h, int I, int j)
{ int f;
f= (g+h)-(i+j);
return f;
}
.TEXT
LDR R4,=F
MOV R0, #5 ;G
MOV R1, #10 ;H
MOV R2, #1 ;I
MOV R3, #4 ;J
; PASS PARAMETRS TO STACK
SUB R13, R13, #16
STR R0, [R13,#12]
STR R1, [R13,#8]
STR R2, [R13,#4]
STR R3, [R13,#0]
BL example
STR R0, [R4]
SWI 0X011
example:
LDR R5,[R13,#0] ; J
LDR R6,[R13,#4] ; I
LDR R7,[R13,#8] ; H
LDR R8,[R13,#12] ; G
ADD R9, R7, R8 ; G+H
ADD R10, R5, R6 ; I+j
SUB R11, R9, R10 ;F= (G+H)-(I+J)
MOV R0, R4 ;RETURNS F THROUGH R0.
ADD R13, R13, #12
MOV PC, LR
.DATA
F: .WORD 0

## Slide 8
THANK YOU
Team MPCA
Department of Computer Science and Engineering